Preliminary Hg Target System - Normal Operations Scenario

| Time (sec.) | Solenoid | Target Pump System | Proton Beam | Optical Diagnostic |
| --- | --- | --- | --- | --- |
|  | Cryogenics | Power Supply |  |  |  |
| minus 40 | Magnet full of LN2 @ 80ºK | Standby | Standby | Call for beam | Off |
| 0-30.0 | Purge LN2 with gaseous He | Standby | Ramp pump to 25 gpm (1.6 l/s) | Wait for beam | Standby |
| 30.0-39.5 | Magnet full of He gas | Ramp to full current | Maintain 20 m/s jet velocity | Wait for beam | Turn on laser back lighting |
| 39.5-40.5 | Magnet full of He gas | Maintain full current | Maintain 20 m/s jet velocity | 24 GeV, 1 MW | Turn on high speed camera |
| 40.5-41.0 | Magnet full of He gas | Begin de-energizing | Shut down pump | Standby | Turn off back light and camera |
| 41.0-45.0 | Magnet full of He gas | De-energize to zero | Turn on heat exchanger | Standby | Off |
| 45.0-1800.0* | Fill magnet with LN2 @ 80ºK | Cool down to ~80°K | Cool Hg to room temperature | Standby | Off |

* Assumes a 30-minute dwell period.

The graph below shows an operating cycle for the solenoid and is shown here to correlate the first column (Time) in the table above, to a physical time scale. T=30 s in the table corresponds to T=0 s in the graph; and T=45 s corresponds to T=15 s, respectively.